## Slide 1: An Introduction to GENI and ExoGENI
Ibrahim Matta, Boston University
Violet Syrotiuk, Arizona State University
Thanks to Vic Thomas, Chip Elliott, Paul Ruth, and others!

## Slide 2: Outline
What is GENI?
How is GENI being used?
What’s next?
Two hands-on exercises:*
  Getting started in ExoGENI with Flukes and in preparation for stitching ExoGENI and Chameleon
  A routing exercise
* You need to have a GENI account and ssh keys installed; if you don’t, instructions provided later!

## Slide 3: GENI – National Infrastructure for Research in Next-Gen Networked Systems

## Slide 4: Slicing and Deep Programmability
Install the software you want throughout your network slice
(into firewalls, routers, clouds, …)
And keep your slice isolated from others,
so they don’t interfere

## Slide 5: Interconnected GENI Hardware
GENI Racks
(50+ campuses
plus regionals)
Research LTE Deployments
(20+ installations)
OpenFlow switches
(50+ campuses, regionals,
and national footprint)

## Slide 6: What Research does GENI Support?
Novel security (Schulzrinne)
Software defined infrastructure (Zink)
Edge clouds (Calyam)
Future internet architectures
driven by wireless (Raychaudhuri)

## Slide 7: GENI Growth
Over 14,000
users
(June 2018)

## Slide 8: NSF Cloud Infrastructure
Kate Keahey
Rob Ricci

## Slide 9: What is Chameleon/CloudLab?
A “meta-cloud” or “cloud factory”
  not a cloud itself
  rather, a facility for trying many kinds of clouds in parallel
Gives bare-metal access and control over a substantial set of computing, storage, and networking resources
Researchers can install standard cloud software stacks, modify them, or create entirely new ones

## Slide 10: The Rise of Global Interoperability
Building a multi-national group of FIDC testbeds, seeking new partners, working from a basis of equality to expand opportunities for researchers worldwide.
Building a multi-national group of FIDC testbeds, seeking new partners, working from a basis of equality to expand opportunities for researchers worldwide.
Working together as peers and equals to expand opportunities for researchers worldwide

## Slide 11: What’s Next?
These are interesting times!
  Major trends are converging in software defined infrastructure
  Economics favors pervasive computation and storage, i.e., “cloud-in-the-loop”
  In 20 years, we expect much fuller spectrum occupancy than today
A deep transformation of the Internet is now underway

## Slide 12: Outline
What is GENI?
How is GENI being used?
What’s next?
Two hands-on exercises:*
  Getting started in ExoGENI with Flukes and in preparation for stitching ExoGENI and Chameleon
  A routing exercise
*You need to have a GENI account and ssh keys installed

## Slide 13: Hands On Exercises
Exercise #1
Getting Started in ExoGENI
Connect to a wireless network:
eduroam or utguest
Go to the GENI Portal and login:
Install ssh keys (if you don’t already have them).
  http://portal.geni.net
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 14: Getting Started in ExoGENI
Click your name in the upper right corner and choose “Profile” from the dropdown menu
Click SSL in the grey bar, then
Click “Create an SSL certificate”
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 15: Getting Started in ExoGENI
Click “Generate Combined Certificate and Key File”
Click
here
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 16: Getting Started in ExoGENI
Download your certificate and key; this creates a pem file that is named “geni-<your_login>.pem”
Save it to a known location on your machine (suggestion: ~/.ssl/geni-<your_login>.pem) Ensure that the .pem file has the appropriate permissions (chmod 0600 ~/.ssl/geni-<your_login>.pem)
Click
here
Now, you can use your pem file to access ExoGENI!
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 17: Generate SSH key-pair
You can generate SSH keys using “ssh-keygen –t rsa”. Please remember the password you have used, it will be required to login to the nodes you reserve. Also, note the location of the public and private key files (default: ~/.ssh/id_rsa, and ~/.ssh/id_rsa.pub).
  You can also generate SSH keys through the GENI Portal: Click “SSH Keys” in the grey bar, and follow the instructions to download your public and private key files.
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 18: Install/Configure Flukes
Install Java on your system if it is not already there:
  OpenJDK is not recommended
  Instead install Oracle JDK 7 or 8 for your platform
  https://www.java.com/en/
Download the Flukes jnlp file:
wget http://geni-images.renci.org/webstart/flukes.jnlp
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 19: Install/Configure Flukes
Edit (create) a ~/.flukes.properties file
Copy/paste the following and edit to point to your GENI pem file and your ssh keys
orca.xmlrpc.url=https://geni.renci.org:11443/orca/xmlrpc user.certfile=/Users/<your_login>/.ssl/geni-<your_login>.pem
user.certkeyfile=/Users/<your_login>/.ssl/geni-<your_login>.pem
enable.modify=true
ssh.key=~/.ssh/id_dsa
# SSH Public key to install into VM instances
ssh.pubkey=~/.ssh/id_geni_ssh_rsa.pub
# Secondary login (works with ssh.other.pubkey)
ssh.other.login=<your_login>
# Secondary public SSH keys
ssh.other.pubkey=~/.ssh/id_geni_ssh_rsa.pub
# Should the secondary account have sudo privileges
ssh.other.sudo=yes
# Path to XTerm executable on your system
xterm.path=/opt/X11/bin/xterm
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 20: Install/Configure Flukes
Run the jnlp by double clicking the file or by using the javaws application on the command line
At this point the Flukes GUI should be running
You may need to create security exceptions on your system to allow it to run; there may also be warnings about certificate authorities
Usually clicking “run” or “continue” in the popup windows works
javaws /path/to/the/file/flukes.jnlp
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 21: Hands On Exercises
Exercise #2
IPv4 Routing on ExoGENI
Our first step is to set up a slice using ExoGENI resources and configure it:
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 22: IPv4 Routing on ExoGENI
Start Flukes (see Step 5, slide 19)
Click in the canvas to place the first VM in the request
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 23: IPv4 Routing on ExoGENI
Right click the new node and choose “Edit properties” from the menu
  If prompted for a password, it is probably empty
Press “OK"
Select:
XO Medium
Centos 7.4 v1.0.3
System select
NodeA
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 24: IPv4 Routing on ExoGENI
Click in the canvas to place two more VMs.
Click and drag a line from each node to the other two nodes. This creates a point-to-point Ethernet between each pair of nodes.
Edit the properties of each node.
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 25: IPv4 Routing on ExoGENI
In addition, set the link properties for each VM.
  For NodeA, set Link1 IP address to 192.168.1.10/24 and Link3 IP address to 192.168.3.10/24
  For NodeB, set Link1 IP address to 192.168.1.11/24 and Link2 IP address to 192.168.2.11/24
  For NodeC, set Link2 IP address to 192.168.2.12/24 and Link3 to 192.168.3.12/24
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 26: IPv4 Routing on ExoGENI
Name your slide by putting a short string in the text box next to the Slice Operations button (suggestion: <yourlogin>.test1).
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 27: IPv4 Routing on ExoGENI
Select “Submit Changes” from the “Slice Operations” dropdown menu. After a few seconds, a window will popup showing the resources you have been assigned (Note: this may take some time).
Click “OK”.
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 28: IPv4 Routing on ExoGENI
Select “View Manifest as List” from the “Slice Operations” dropdown menu. A window will popup listing the status of your requested resources. The status could be: Ticketed, Active, or Failed. Ticketed resources are not yet ready. Active resources are ready to use. Failed resources experienced a problem that prevented it from becoming Active.
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 29: IPv4 Routing on ExoGENI
Once the resources are Active, if your xterm or putty configuration is correct you can login to any of the VMs by right clicking the VM and choosing “Login to Node”. Alternatively, you can right-click the node and choose “View Properties” to see the public IP address of the VM. You can then ssh to the VM using that address and the private key that corresponds to the public key you referenced in your .flukes.properties file.
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 30: IPv4 Routing on ExoGENI
Login to one of the VMs, and try pinging another VM.
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 31: IPv4 Routing on ExoGENI
Setup the routing so packets from A sent to IP address 192.168.2.12 on node C should be routed via node B. In order to create this routing behavior you will need to modify the routing tables in your nodes using the Linux route command
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 32: IPv4 Routing on ExoGENI
To install “traceroute” on Centos 6/7:
  yum install traceroute –y
  (Type “which traceroute” to verify installation)
A useful tool to debug the packet flow is ​tcpdump. In order to install it run:
  yum install tcpdump
  (To observe packet flow on an interface, type “tcpdump –i ethX”. Run “ifconfig” to examine the IP addresses and names of interfaces of a VM.)
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 33: IPv4 Routing on ExoGENI
On Node A, add a static route to Node C 192.168.2.12 using as gateway node B 192.168.1.11
  sudo route add –net 192.168.2.0 netmask 255.255.255.0 gw 192.168.1.11
On Node B, enable IP forwarding:
  sudo sh –c ‘echo 1 > /proc/sys/net/ipv4/ip_forward’
On Node C, setupm traffic for Node A 192.168.1.10 through node B 192.168.2.11
  sudo route add –net 192.168.1.0 netmask 255.255.255.0 gw 192.168.2.11
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 34: IPv4 Routing on ExoGENI
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 35: IPv4 Routing on ExoGENI
Select “Delete Slice” from the “Slice Operations” dropdown menu to release your resources so that other experimenters can use them. Press “OK”.
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment